Connection Reference for 9030

Version 2.0

2010/03/01  V2.0

Contents

§1  9030 dimensions instructions	3

§2  9030 block diagram	3

§3  motor control signals	5

§3.1 Encoder input signals	6

§3.2 pulse output signals	7

§3.3 servo_on output	7

§4  PWM/DA output	8

§5  MPG connector	9

§6  General purpose IO	10

§7  anti-interference	12

§8  9030 Card vulnerable components	12

# §1  9030 dimensions instructions

unit: mm

Figure1 9030 dimension

# §2  9030 block diagram

|  |  |  |  | ＋5V |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | GND |  |
|  |  |  |  | GND +24V |  |

Note：

1.  +5V：connected to extra power supply ＋5V

2.  +24V：connected to extra power supply ＋24V

3.  GND：connected to extra power supply reference GND

4.  JD1～JD4：motor controlling PORT

5.  JD5：Manual Pulse Generator Port

6.  JD6：GPIO PORT（24 DI， 8DO）

7.  J9、J10：JUMPER for setting PWM or DA out mode

8.  PWM/GND ：PWM out port as default，also can output one channel DA（-10V ～ +10V）in that case，the extra power +12V/-12V is integrant

# §3  motor control signals

Each axis of  9030 card can work in two modes: open_loop mode and semi_closed_loop. in these two modes, 9030 card all outputs pulse. Must connect the encoder signals to the 9030 card when it works under semi_closed loop mode.

Figure3.1 JD1~JD4 diagram

Table 1.3.1 axes signals definition

| Name | direction | definition |
| --- | --- | --- |
| A- | in | Encoder Phase A- |
| A+ | in | Encoder Phase A+ |
| B- | in | Encoder Phase B- |
| B+ | in | Encoder Phase B+ |
| Z- | in | Encoder Phase Z- |
| Z+ | in | Encoder Phase Z+ |
| +5V | out | +5V Power |
| PLUS | out | Output pulse CW/Pulse+ |
| /PLUS | out | Output pulse CW/Pulse- |
| SIGN | out | Output pulse CCW/DIR+ |
| /SIGN | out | Output pulse CCW/DIR- |
| ALM | in | Alarm input |
| GND |  | Gnd |
| SVon | output | Servo_on output |
| SV COM | Servo_on common GND | Servo_on common GND |
| shield |  | shield(GND) |

### §3.1 Encoder input signals

figure3.2 Circuit Diagram of Encoder Feedback

### §3.2 pulse output signals

figure.3.3 Line Driver Input Interface

### §3.3 servo_on output

figure3.5  servo on diagram

# §4  PWM/DA output

9030 has one channel PWM or DA output which can be settled by jumper J9, J10.

| JUMPER | J9, J10 |  |
| --- | --- | --- |
| PWM out | Pin2 and Pin 3 short (Default) |  |
| DA out | Pin1 and Pin 2 short | Note you should supply +12V/-12V power when you use the DA output,and the GND is defined as AGND |

# §5  MPG connector

DB15 connector diagram：

Pin definition：

| Name | Definition | Explain |
| --- | --- | --- |
| 1 | A+ | MPG Phase A+ |
| 9 | A- | MPG Phase A- （unplug when Single-ended encoder input） |
| 2 | B+ | MPG Phase B+ |
| 10 | B- | MPG Phase B- （unplug when Single-ended encoder input） |
| 3 | GND |  |
| 11 | +5V |  |
| 4 | I25(REV) | GPI |
| 12 | I26(Xsel) | GPI (X axis selected , defined in WinCNC) |
| 5 | I27(Ysel) | GPI (Y axis selected , defined in WinCNC) |
| 13 | I28(Zsel) | GPI (Z axis selected , defined in WinCNC) |
| 6 | I29(Wsel) | GPI (W axis selected , defined in WinCNC) |
| 14 | I30(Multi×1) | GPI(pulse×1, defined in WinCNC)) |
| 7 | I31(Multi×10) | GPI(pulse×10, defined in WinCNC)) |
| 15 | I32(Multi×100) | GPI(pulse×100, defined in WinCNC)) |
| 8 | GND |  |

# §6  General purpose IO

（1）JD6 (DB37) pin diagram：

（2）General purpose Input

9030 accepts the passive node as the input signal. when the switch is applied, the internal +5V will source the photo coupler

Figure6.1  circuit diagram for input

When you use the photo sensor as input switch,plesase choose the type of DC NPN . The following figure is an example of photo sensor used in the case of limit switch input.

Figure6.2 photo sensor used as input

（3）General purposeOutput

Figure6.3 output circuit diagram

# §7  anti-interference

Be sure to take the following measures to prevent interference：

- The Servo drive’s signal cables are made of shielded cables, and make sure that servo drive’s signal cable shielding is effectively connected with the shell .

The 9030 Card’s 15-pin connector (axis control signal connector) shell should be connected with the signal line shield

- The servo drive enclosure and 24V DC power supply common ground.

# §8  9030 Card vulnerable components

① ULN 2803

② SN75175

# Text boxes

USB

POWER Port

X Axis

3

X轴       JD1

Z-

JD1

3

X轴       JD1

Z-

J10

3

X轴       JD1

Z-

J9

3

X轴       JD1

Z-

3

3

2

3

PWM

3

X轴       JD1

Z-

1

3

JUMPER

PWM port (DA

Port is alternative

－10V～+10V）

Axis controlling port

Y Axis        JD2

Z Axis        JD3

GND

3

X轴       JD1

Z-

+12V

3

X轴       JD1

Z-

-12V

3

X轴       JD1

Z-

W/A Axis

JD4

3

X轴       JD1

Z-

GPIO

JD5

3

X轴       JD1

Z-

JD6

3

X轴       JD1

Z-

MPG Port

DB 37F

3

X轴       JD1

Z-

1

2

9

10

11

3

12

4

13

5

14

6

15

7

8

SV_COM

SVon

GND

ALM

SIGN

/PULS

PULS

+5V

Z+

B+

B-

A+

A-

/SIGN

shield

Z-

Encoder

9030 card side

Shell

Shell

9030 side

Motor driver side

Motor driver side

9030 side

Motor driver side

9030 Card Internal circuit

1

2

9

10

11

3

12

4

13

5

14

6

15

7

8

GND

I32(Multi×100)

I31(Multi×10)

I30(Multi×1)

I29(Asel)

I28(Zsel)

GND

+5V

B-

B+

A-

A+

I27(Ysel)

I26(Xsel)

I25

1

2

20

21

22

3

23

4

24

5

25

6

26

7

8

I1

I15

I2

I14

I3

I13

I6

I11

I10

I7

I9

I8

I4

I12

27

9

28

10

29

11

30

12

31

13

32

14

33

15

34

16

35

17

36

18

37

19

I5

GND

I16

I22(ALM1)

GND

I18

I20

GND

I19

I17

I21(ALM0)

I23(ALM2)

I24（ALM3）

O8

24V

24V

O1

O2

O3

O4

O5

O6

O7

+5V

+5VEX

GND

I1-I32

switch

MCU

9030 internal circuit

－

+

ｏ

DC12~24V

I1~I20

GND

+24V

+5V

Imax = 500mA

OUT1-8

COM

Darlington

9030 internal circuit

1 x ULN2803

4 x SN75175